## Slide 1
DA3 REVISION
DATA BALANCING & AUGMENTATION
STRATEGIES FOR HOTSPOT DETECTION
Lithography Hotspot Detection on the ICCAD-12 Benchmark: Revised per Reviewer Feedback
BEVD402L: AI and Machine Learning for IC | Digital Assignment III | Group 11
Priyanuj Boruah
23BVD1066
Kartik Aggarwal
23BVD1067
Code: https://github.com/<your-github-username>/Lithography-Hotspot-Detection-G11

## Slide 2
Agenda
01
The Problem
Lithography hotspots & severe class imbalance
02
What We Revised
Validation split, equal steps, seeds, PR-AUC
03
Method
Common CNN backbone + 8 balancing strategies
04
Results
Main comparison across 5 benchmarks, 3 seeds
05
Key Findings
Why DA2's conclusions changed
06
Feedback Addressed
Every reviewer point, mapped to our response
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
2

## Slide 3
The Problem: Lithography Hotspots
Photo-lithography prints chip layouts onto silicon.
As transistors shrink, some layout patterns become too fine to print correctly.
A “hotspot” is a layout region likely to print as a broken (open) or shorted (bridging) circuit
Catching hotspots early avoids costly re-spins and mask corrections
Full lithography simulation is accurate but far too slow for full-chip checks
→ Machine learning offers a fast screening alternative
SIMPLIFIED LAYOUT CLIP
HOTSPOT
(pinch risk)
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
3

## Slide 4
The Real Challenge: Severe Class Imbalance
ICCAD-12 test-set imbalance ratio (Non-Hotspot : Hotspot)
B1
20.7:1
NHS : HS
226 HS
4,679 NHS
B2
82.9:1
NHS : HS
498 HS
41,298 NHS
B3
25.6:1
NHS : HS
1808 HS
46,333 NHS
B4
180.2:1
NHS : HS
177 HS
31,890 NHS
B5
471.4:1
NHS : HS
41 HS
19,327 NHS
A classifier that always predicts “Non-Hotspot” scores >99% raw accuracy on B5, and catches zero hotspots. This is why Balanced Accuracy and PR-AUC, not accuracy, drive this whole study.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
4

## Slide 5
OUR RESEARCH QUESTION
Which data-balancing strategy provides the most effective improvement for highly imbalanced ICCAD-12 hotspot detection?
DA3 revision: our DA2 answer was contaminated by an unfair training protocol. This talk is as much about that correction as it is about the original question.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
5

## Slide 6
Common Classification Backbone
Identical lightweight CNN for every strategy isolates the effect of the training data
Input
64×64×1
grayscale
→
Basic Block 1
3× Conv(3×3,12)
+BN +ELU +Pool
→
Pool
downsample
→
Basic Block 2
3× Conv(3×3,12)
+BN +ELU +Pool
→
FC Head
Flatten→Dropout
→FC(10)→FC(1)
8,649
trainable parameters
PyTorch
re-implementation
Equal steps
not epochs: fixed per-benchmark gradient-update budget for every strategy (DA3)
Same order of magnitude as the reference paper's custom CNN (12,873 params). A held-out validation split now selects the training checkpoint; the test split is touched exactly once per run.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
6

## Slide 7
Eight Data Strategies, One Fair Comparison
Two new combined variants added in direct response to DA3 feedback
1
Baseline
Natural imbalance, no intervention
2
Random Undersampling
Discard majority (NHS) samples
3
Random Oversampling
Duplicate minority (HS) samples
4
Oversampling + Aug.
Duplicate + flip/rotate HS
5
Balanced Mini-Batch
Sampler forces ~50:50 per batch
6
Combo (50% US)
Undersample NHS + aug-oversample HS
7
Combo-Mild (25% US)
Same, milder undersampling
8
Combo (Batch+Aug)
Balanced batch + stochastic aug.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
7

## Slide 8
Experimental Protocol (Revised)
1
Val. Split
15% of training data carved out; fixed split seed shared by every strategy/seed
→
2
Equal Steps
Every strategy trains for the same gradient-update budget per benchmark, not epochs
→
3
3 Seeds
42, 123, 2024: checkpoint picked on validation; test touched once
→
4
PR-AUC + Sig. Test
Threshold-free ranking metric + paired t-test / Wilcoxon, α=0.05
Grid size: 5 benchmarks × 8 strategies × 3 seeds = 120 main runs, + 75 ratio-ablation runs + 9 learning-curve runs (204 total training runs, vs. 30 in DA2)
Key fix: DA2 trained every strategy for a fixed 8 epochs, but RUS's smaller resampled dataset meant far fewer actual gradient updates per epoch than ROS. That confound is now removed.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
8

## Slide 9
Results: Average Performance (5 Benchmarks × 3 Seeds)
Chart: 
| Baseline | RUS | ROS | ROS+Aug | Bal.Batch | Combo(50%) | Combo(25%) | Combo(B+A)
Balanced Acc. | 0.922 | 0.928 | 0.936 | 0.917 | 0.937 | 0.924 | 0.931 | 0.934
Recall | 0.94 | 0.974 | 0.967 | 0.926 | 0.971 | 0.952 | 0.957 | 0.96
Specificity | 0.905 | 0.883 | 0.905 | 0.908 | 0.903 | 0.895 | 0.904 | 0.908
PR-AUC | 0.664 | 0.492 | 0.75 | 0.663 | 0.718 | 0.649 | 0.658 | 0.681
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
9

## Slide 10
Results: Balanced Accuracy per Benchmark
Chart: 
| B1 | B2 | B3 | B4 | B5
Baseline | 0.811 | 0.986 | 0.963 | 0.929 | 0.923
RUS | 0.81 | 0.978 | 0.958 | 0.937 | 0.957
ROS | 0.808 | 0.984 | 0.957 | 0.962 | 0.969
ROS+Aug | 0.804 | 0.975 | 0.968 | 0.938 | 0.901
Bal.Batch | 0.808 | 0.99 | 0.958 | 0.958 | 0.971
Combo(50%) | 0.806 | 0.93 | 0.957 | 0.949 | 0.975
Combo(25%) | 0.806 | 0.973 | 0.959 | 0.961 | 0.955
Combo(B+A) | 0.807 | 0.971 | 0.965 | 0.953 | 0.974
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
10

## Slide 11
KEY FINDING #1
Once training is fair, balanced accuracy barely tells strategies apart
DA2 (unequal updates, 1 seed)
0.779 – 0.945
17-point spread: looked like strategy choice mattered a lot
RUS appeared to collapse to 0% recall on the most extreme benchmark. That was our DA2 headline claim.
DA3 (equal steps, 3 seeds)
0.917 – 0.937
2-point spread. NO pairwise comparison is statistically significant (α=0.05)
RUS now reaches 0.957 balanced accuracy on that same benchmark. The DA2 “collapse” was a training-protocol artifact, not a property of undersampling.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
11

## Slide 12
Key Finding #2: Why RUS “Failed” in DA2: A Mechanistic Look
Per-step learning curves on Benchmark 5, across 3 seeds
RUS memorizes its tiny resampled pool (~44 images) almost immediately: training loss crashes near-zero within ~150 steps. Its validation recall peaks by step ~73 and then degrades with further training if left unchecked.
The Baseline, by contrast, needs the entire step budget just to start detecting hotspots at all: its gradient signal from the rare positive class is heavily diluted by the natural imbalance. DA2's fixed-epoch, no-checkpoint protocol evaluated RUS at the wrong point in training.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
12

## Slide 13
PR-AUC Reveals What Balanced Accuracy Hides
Statistically significant differences (paired t-test + Wilcoxon, both p<0.05)
Comparison (PR-AUC)
Mean A
Mean B
Result
ROS vs. RUS
0.750
0.492
p=0.0048
Bal.Batch vs. RUS
0.718
0.492
p=0.019
ROS vs. Baseline
0.750
0.664
p=0.033
ROS vs. ROS+Aug
0.750
0.663
p=0.0025
Combo(B+A) vs. RUS
0.681
0.492
p=0.027
Once we stop relying on a single 0.5 threshold and look at ranking quality across every threshold, RUS is reliably worse than oversampling-based strategies, just not in balanced accuracy.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
13

## Slide 14
Feedback Addressed
Every reviewer point for Group 11, mapped to what we did
✓
Validation split + equal gradient updates
Done: 15% validation carve-out, step-based training, checkpoint selection
✓
Add seeds
Done: 3 seeds (42/123/2024), paired t-test + Wilcoxon significance tests
✓
Test combined strategies + PR-AUC
Done: 3 combined variants (50%/25%/Batch+Aug); PR-AUC on every run
✓
Justify augmentations physically
Done: Manhattan-geometry closure + local-diffraction-physics argument
✓
Explain mechanistically why RUS fails
Revised: it doesn't, once trained fairly; learning curves show why DA2 was wrong
✓
30–35+ references, validation-only tuning, published comparison
Done: 40 refs, test touched once, compared vs. 2 published ICCAD-12 detectors
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
14

## Slide 15
Ablation: Effect of the Target Class Ratio
Sweeping HS:NHS target ratio 0.1–1.0 for RUS, ROS+Aug, Combo (single seed)
RUS now stable across every ratio
Recall/specificity stay high (≥0.90 / ≥0.95) on B5 at every tested ratio, a complete reversal of the DA2 ablation, which showed RUS stuck at 0% recall regardless of ratio.
But RUS's PR-AUC still degrades with aggressive undersampling
On B5, RUS's PR-AUC falls from 0.80 (mild ratio) to ~0.08–0.11 (aggressive ratios) even while balanced accuracy stays flat. That is the ablation-level confirmation of the mechanistic story.
Combined strategy is flat across ratios, no DA2-style collapse
No ratio on any benchmark reproduces DA2's dramatic collapse-and-recover pattern; remaining variation is single-seed noise, a limitation we flag directly.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
15

## Slide 16
CONCLUSIONS
A more cautious, more honest answer than DA2
1
Balancing strategy matters far less than DA2 suggested
Under fair training, no strategy's balanced accuracy is statistically distinguishable from any other's, including the baseline. Most of our DA2 spread was a protocol artifact.
2
PR-AUC recovers real, significant structure
Oversampling-based strategies (ROS especially) significantly outperform RUS on ranking quality, even though their balanced accuracies are statistically tied.
3
RUS's real weakness is calibration, not detection
Its tiny effective training set makes probability outputs fragile and poorly ranked: a narrower, more defensible mechanistic claim than DA2's “fails outright.”
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
16

## Slide 17
Thank You
Questions & Discussion
CODE & REPRODUCIBILITY
https://github.com/<your-github-username>/Lithography-Hotspot-Detection-G11
Full code, cached data, figures, significance tests, and the IEEE-format report are in the repository above.
Group 11 (DA3 Revision) · Data Balancing and Augmentation Strategies for Hotspot Detection
17